APPENDIXE

FOREST FIRE RISK ASSESSMENT

Parameters for the forest fire risk assessment

Forest fire risk assessment measures include the following parameters:

1. Vegetative covering,

2.  Anthropogenic factors,

3.  Clime,

4.  Place (matrix substratum and type of soil),

5.  Relief and

6.  Forests collocation.

1.   Taking into consideration different forms of the components (according to the type of woods, the way of forming, administration way, cultivation way, dedication etc), forestry vegetation is gathered to the components of coniferous and deciduous forests as well and mixed components are also taken the cultivation forms such as: shrubs, bushes, and plantation with other crops that are specific regarding the forest fire sensitivity.

2.   Looking according to the statistics the biggest percentage of the fire causers in forests  are directly linked with the activity of human (anthropogenic factors), thus this parameter is divided in three categories, with determined number of points.

3.   Climatic factor is composed by three parameters: annual mid climatic temperature, atmospheric rainfalls quantity and air moisture.

4.   Matrix substrate and type of the land are also taken as special parameters which affect the forest fire risk level. Forest fire risk level depends on content of moisture in the material that is being burnt on land (trunk, leaf, brunch, roots etc) whereas moisture level is changed by different lands, respectively in matrix substratum.

5. Relief with its factors has a big impact of the forest fire risk. Intensity and duration of the insulation affect to the acceleration of drying material for burning, and this one is different depending on inclination exhibition. The attitude above sea in which is located the content is taken like reading of annual mid temperature.

6.   Holding of forestry collocation also impact to the forest fire risk level. In forests where the forestry collocation it is not being held comes till to the increase of quantity of material for burning, and with this also comes to the raised consignment for the fire.

Influence of all factors included is expressed with numbers of the points whose value is less than 115, and more than 580 points.

Depending on number of points, all Kosovo forests, according to the forest fire risk are classified in four levels:

| LEVEL | RISK | NUMBER OF POINTS |
| --- | --- | --- |
| I | VERY LARGE | More than 480 |
| II | LARGE | 381 - 480 |
| III | AVERGAE | 281- 380 |
| IV | SMALL | Up to 280 |

Regarding the measures, there is given the textual overview and description of included and classified factors according to the intensity of the forest fire risk influence as well and number of the appropriate points.

MAIN PARAMETRES ON FOREST FIRE RISK ASSESSMENT

1. VEGETATION

| Vegetation (type of components ) | Figure, class of time frame of the settlement | Number of points |
| --- | --- | --- |
| 1.1. | Coniferous forests | H,I,J | 200 |
| 1.1.1. | Coniferous forests crops |  |  |
| 1.1.2. | Helophyte coniferous forests (pine, larch, cypress) |  |
| 1.1.2.1. | Up to 30 years | D3 and 6 | 200 |
| 1,1,2,2, | 31-60 years and other ages | D4 | 180 |
| 1,1.2.3. | More than 60 years | C1 and 2 | 160 |
| 1.1.3. Sciophyte coniferous forests (fir, juniper,) |
| 1.1.3.1. | Up to 30 years | C3 and 6 | 160 |
| 1.1.3.2. | 31-60 years and the other ages | D4 | 140 |
| 1..1.3.3. | More than 60 years | C1 and 2 | 120 |
| 1.2. Mixed components (forests with pine and Norway spruce) |
| 1.2.1. | Mixed crops | B | 180 |
| 1.2.2. Mixed components helophyte (pine, larch, oak, soft deciduous) |
| 1.2.2.1. | Up to 30 years | B3 and 6 | 180 |
| 1.2.2.2. | 31 – 60 years | B4 | 100 |
| 1.2.3. Mixed forests sciophyte (fir, juniper, beech wood) |
| 1.2.3.1. | Up to 30 years | B3 and 6 | 120 |
| 1.2.2.2. | 31 – 60 years and their ages | B4 | 100 |
| 1.2.3.3. | More than 60 years | B1 and 2 | 80 |
| 1.3. Deciduous forests components |
| 1.3.1. | Crops an deciduous plantation | G, K | 120 |
| 1.3.2. | Heliophyte deciduous components | F5 and 7;E5 and 7, |  |
|  | (oak, soft deciduous ) | M2 and 3 | 120 |
| 1.3.2.1. Degraded components |
| 1.3.2.2. | 31- 60 years | E4,F4, M1 | 100 |
| 1.3.2.3. | More than 60 years | E1, 2, F1 and 2 | 80 |
| 1.3.3. | Sciophyte deciduous components (beech wood) |
| 1.3.3..1. Degraded forests components | A5 and 7;L2 and 3 | 80 |
| 1.3.3.2 | Up to 30 years | A3 and 6 | 80 |
| 1.3.3.3. | 31 and 60 years and other ages | A4 and L1 | 60 |
| 1.4. | (maki and garigu ) | N,O | 200 |
| 1.5. | Shrubs and bushes | P, R | 160 |
| 1.6. Unprocessed Forestry Land | S | 80 |

Type of the components, classes of the old age and settlement

1. Components of the old age:

A – Beech wood

B - Mixed

C - Juniper

D – Pine

E - Oak

F – Soft deciduous

A –f: 3 and 6 – other components (up to 30 years)

4 – Components of mid age (31 – 60 years of the old age)

1.2 – Maturity components (more than 60 years)

5.7. – Degraded components

2. Crops

G – Acacia

H - Pine

I - Juniper

J – Coniferous

K – Other deciduous

3. Trunks

L – Beech wood

M - Oak

L and M:             1- Conserved

2 – Degraded

3 – Protected

4. Degraded components

P - Shrubs

R - Oar

S - Unprocessed forestry land

Crops and plantation are artificially raised forests and regardless the old age, almost are risked by the fire into forests.

Components of pines are considering those in which participation of coniferous is less than 90%.

In the helophyte coniferous component are counting forests such as: pines, cypress, larch, and other types with lightness color.

In the sciophyte forests components are counting forests such as: fir, juniper, yew – tree and other types that are being planted.

Mixed components are those forests in which the pines and deciduous contain more than 10%.

Forests sciophyte mixed components are those which mainly contain the types of coniferous and deciduous as well and may be planted.

Deciduous forests are those forests in which are represented at least 90%.

2. ANTROPOGEN FACTORS

2.1. Category I – forests cultivation for tourist places and recreation, parks and national reservations, forests that are directly being located near to the storages of wastes and agriculture lands.

Number of points 60

2.2. Category II – forests in which pass the public roads or long conductors or where the pasturage is being done. .

Number of points 40

2.3. Category III – forests in which are collected forests secondary products shall be done the hunting, fishing as well and meliourous and cultivation works.

Number of points 20

If one of the components, according to the risk form human may be ranged in many categories, risk from the fire is gained with counting of the points of those categories.

3. CLIMATE

|  | Number of points |
| --- | --- |
| 3.1. Mid annual temperature |  |
| 3.1.1. | above12 C | 30 |
| 3.1.2. | 9,1 – 12 C | 20 |
| 3.1.3. | Up to 9,0 C | 10 |
| 3.2. Mid rainfalls annual quantity |
| 3.2.1. | Up to 800 mm | 30 |
| 3.2.2. | 8001 – 1200 mm | 20 |
| 3.2.3. | above 1200 mm | 10 |
| 3.3. Mid annual moisture of the relative air |
| 3.3.1 | above 70% | 30 |
| 3.3.2. | 71 – 80% | 20 |
| 3.3.3. | above 80% | 10 |

4. DWELLING – PLACE (matrix substratum and type of land)

4.1. Category I                                                                number of points 80

4.1.1. Moveable gravel

Rendzina (type of land) (pararendzina in the fuel gravel)

Ranker in the gravel of quartz and silicate

4.1.2. Dolomite                                                        number of points 60

4.2. Category II

4.2.1. Dolomite and limy stability

Black land, superficial and deep average

Terra fusca and terra rosa (red) in limy land

4.2.2. Acid eruptive rocks (granite, sijeniti, trahiti rioliti etc.)

Ranker district (acid land humus silicate)

4.2.3. District rocks (gabbros, basalt, periodic, serpentine etc,)

Black land

4.3. Category III

4.3.1. Dolomite and limy

Black land, deep

Black land

4.3.2. Dry eruptive rocks

Black acid land, deep

Black land and black land acid,

Deeply on the average

4.3.3. Basic eruptive rocks

4.3.4. Components of black lands rivers

Number of points 20

4.4. Category IV

4.4.1. Dry rocks silicate (gnajs, fili, stone slab etc.)

Acid black land, very deep

Humus acid black land

Black land, deep very deep

4.4.2. Argil (Pleistocene and Pliocene)

Pseudoglej

Black land

Semiglej

Euglej

4.4.3. Fluvit material and fluviglacial, material average eolsik (blackland

fens)

Pseudoglej

Euglej

Paludal black land (homoglej)

Alluvia (fluxion)

Tubby land (mineral or with the coal)

5. RELIEF

|  | Relief parameter | Number of points |
| --- | --- | --- |
| 5.1. Exhibition |  |
| 5.1.1. | South and field | 20 |
| 5.1.2. | East and west | 10 |
| 5.1.3. | North | 5 |
| 5.2. The aptitude above sea |  |
| 5.2..1. | Up to 500 m | 15 |
| 5.2.2. | 5001 – 800 m | 10 |
| 5.2.3. | Above 800 m | 5 |
| 5.3. Inclination |  |
| 5.3.1. | More than 45 | 15 |
| 5.3.2. | 31 - 45 | 10 |
| 5.3.3. | 15 - 30 | 5 |

6. FORESTRY COLLOCATION

|  | Type of the components | Number of points |
| --- | --- | --- |
| 6.1. | Unregulated | 40 |
| 6.2. | Partly regulated | 20 |
| 6.3. | Regulated | 10 |

Regulated components may be considered those that have built and maintained roads from the fire, roads and paths that are also being regularly cleaned, thinned, pruned brunches in the sidelong parts of the components as well and are reduced tiny material that is being burnt.

Components partly regulated are considered those in which the above mentioned works are partly done.

Unregulated components are also those in which none of the work is being done from the mentioned works.